High-Power Targets — Development and testing of spallation neutron sources

Yacine Kadi, Samec Karel and Yoann Nicolas Fusco – CERN (Engineering Department)

Recent testing of two advanced high-power neutron spallation sources MEGAPIE and EURISOL have yielded a wealth of experimental data and operational experience that is of relevance to efforts currently under-way to develop a safe and reliable target system. The neutron spallation source must be maintenance-free and inherently safe to operate. The radio-toxic inventory in the liquid metal must at all times be contained within successive layered barriers to avert contamination in the event of an accident.

The present contribution reports on the current activities performed within the THIPAC work package  (Test Infrastructure for High Power Accelerator Components) of the FP7 TIARA Project dedicated on planning the infrastructure necessary for testing high power neutron spallation targets. The paper reviews constraints in terms of the general layout of the neutron source and shows how liquid metal neutron source design may be improved compared to the current state of the art.

# Footnotes

The research leading to these results has received funding from the European Commission under the FP7-INFRASTRUCTURES-2010-1/INFRA-2010-2.2.11 project TIARA (CNI-PP). Grant agreement no 261905.